## Slide 1: SimSpect defense specification reference
Guide to defense implementations in SimSpect formal language and model notes

## Slide 2: Contents
For each defense we outline:
Defense overview and paper notes
SimSpect specification of each defense variant
Implementation notes and mechanisms to exercise in test generation
Known bugs (if applicable)
Defenses:
STT [Yu+, MICRO ’19]
SpecShield [Barber+, PACT ’19]
NDA [Weisse+, MICRO ’19]
Delay-on-Miss [Sakalis+, ISCA ’19]
SDO [Yu+, ISCA ’20]
SPT [Choudhary+, MICRO ’21]
Recon [Aimoniotus+, MICRO ’23]
Doppelgänger loads [Kvalsvik+, ISCA ’23]
Protean
Non-applicable defenses
Under construction

## Slide 3: Simple alloy model
Protection set, Leakage contract, and Execution contract
    Relaxations remove instructions, memory/registers, connecting edges from the model
    Have generic speculation primitives, transmitters
    Base of GLIFT-style information flow tracking to conservatively measure protection set propagation through the model

## Slide 4: Speculative Taint Tracking — MICRO ’19
Defines explicit vs. implicit covert channels
Stalls explicit transmitters until youngest load whose return value influences data becomes nonspeculative (YROT)
Blocks implicit branch prediction from operating as a function of tainted data
Blocks implicit branch resolution from transmitting until predicate is nonspeculative
Untaints the output of an access instruction when all older control flow instructions resolve (ctrl speculation) or when access instruction cannot be squashed (does this in 1 cycle)
STT

## Slide 5: SimSpect specification
Protection set: all memory. Propagation: strict dependency + YROT untaint calculus — a. Any speculative access instruction is tainted. b. Other output is tainted if input is tainted. Untainted once YROT nonspeculative. YROT is youngest YROT of args if not AI, or else AI addr. (like DIFT)
Leakage contract: explicit transmitter set user-defined, implicit transmitters also handled by aforementioned prediction and resolution taint blocks
Execution contract: Architect-defined visibility point (at head of ROB, or oldest unresolved branch)
STT

## Slide 6: Mechanisms to exercise
Leakage contract: must complicate transmitter tracking — implicit transmitters are blocked at both prediction and resolution, have two elements for those components and enable probing of relevant state for both
Taint tracking: first example of taint tracking, propagate direct dependencies GLIFT-style through the program
    Basis for the model data-dependency propagation
    Relax the data-dependency edges by removing them
      This is sufficient because we do not check for overprotection, so no point in increasing the number of edges
STT

## Slide 7: Known bugs
Store transmitters
    STT does not consider stores to be transmitters. This is in line with their paper and security definitions but not in line with real life or gem5
STT

## Slide 8: SpecShield — PACT ’19
STL – delays AIs for the duration of speculation, being defined as reaching the head of the ROB
ERP – delays AIs for the duration of speculation, by waiting until all older branches are resolved and nonspeculative and all older loads and stores have no faults (nothing is speculative)
ERP+ – tracks taint and allows low leakage instructions to see AIs of speculative things as long as they don’t pass to high leakage things
Handles speculation primitives: meltdown, branch misprediction, memory alias misprediction, control flow hijacking
ONLY defends memory secrets, not register secrets, through AI provision
SpecShield

## Slide 9: SpecShield-STL SimSpect specification
Protection set: All memory. Propagation: strict dependency — a. Any speculative access instruction is protected. b. Other output is protected if input is protected (conservative because this should not be exercised because cut off at AI)
Leakage contract: Transmitter type irrelevant, should protect for all
Execution contract: Instructions must reach the head of the ROB to become non-speculative
SpecShield

## Slide 10: SpecShield-ERP SimSpect specification
Protection set: All memory. Propagation: strict dependency — a. Any speculative access instruction is protected. b. Other output is protected if input is protected (conservative because this should not be exercised because cut off at AI)
Leakage contract: Transmitter type irrelevant, should protect for all
Execution contract: Instructions are non-speculative at head of ROB, but also before head of ROB if ∄ older unresolved branches, and ∄ unresolved or faulted older loads and stores
SpecShield
Notes: Todo see if it’s unresolved targets or addresses

## Slide 11: SpecShield-ERP+ SimSpect specification
Protection set: All memory. Propagation: strict dependency — a. Any speculative access instruction is protected. b. Other output is protected if input is protected
Leakage contract: High-likelihood transmitters
Execution contract: Instructions are non-speculative at head of ROB, but also before head of ROB if ∄ older unresolved branches, and ∄ unresolved or faulted older loads and stores
SpecShield

## Slide 12: Non-speculative Data Access — MICRO ’19
Two types of attacks
    Control steering, victim control flow leaks its own information
    Chosen code, attacker uses their own code to violate permissions speculatively
An instruction is safe if not after a branch with unresolved target and direction or a store with an unresolved address
When a microop resolves, mark things safe until the next outstanding speculation primitive
    Delay broadcast of outputs until safe
Strict vs permissive propagation version, which only treats loads as AIs (only protects memory)
NDA
Notes: Todo explain why two load blocks are different
Whether or not we have bypass restriction

## Slide 13: NDA-S SimSpect specification
Protection set: all memory and registers. Propagation: strict dependency — a. Any speculative access instruction is protected. b. Other output is protected if input is protected
Leakage contract: Transmitter type irrelevant, should protect for all
Execution contract: Instructions are non-speculative at head of ROB, but also before head of ROB if ∄ older branches with unresolved target or address, and ∄ stores with unresolved address
NDA

## Slide 14: NDA-P SimSpect specification
Protection set: all memory. Propagation: strict dependency — a. Any speculative access instruction is protected. b. Other output is protected if input is protected
Leakage contract: Transmitter type irrelevant, should protect for all
Execution contract: Instructions are non-speculative at head of ROB, but also before head of ROB if ∄ older branches with unresolved target or address, and ∄ stores with unresolved address
NDA

## Slide 15: Delay-on-Miss — ISCA ’19
Blocks speculative loads from transmitting by allowing them to go to L1 cache but no further, so they don’t exhibit data-dependent timing or prime the cache
Doesn’t discriminate between non-speculatively and speculatively acquired secrets
Used value prediction to speed up secure speculation
Has both eager and normal speculation modes
DoM

## Slide 16: SimSpect specification
Protection set: All registers and memory
Leakage contract: Protects against load-address transmission only
Execution contract: Protects instructions that fall under shadows:
    E-Shadows – instructions that can generate exceptions
    C-Shadows – control instructions with an unknown address or condition
    D-Shadows – load dependencies due to stores with unknown addresses because of STL forwarding
    M-Shadows – under strict memory models, load reordering could lead to squashes
DoM

## Slide 17: Speculative Data-Oblivious Execution — ISCA ’20
Insight: Because of STT implicit branch stopping, the predictor is safe. There should be no tainted data affecting a predictor
    Squashes are revealable because they happen only when predicate is no longer tainted
    Only be concerned about explicit transmitters
Translate into a set of transmitter functions that cover path variability, and then predict path based on nonspeculative data (squashes are fine)
Predict based on PC
Loads are the complicated aspect, load function hides timing but not address leakage, must still block these types of leaks
SDO
Notes: Todo answer q about load blocking complexity

## Slide 18: SimSpect specification
Protection set: all memory. Propagation: STT - strict dependency + YROT untaint calculus — a. Any speculative access instruction is tainted. b. Other output is tainted if input is tainted. Untainted once YROT nonspeculative. YROT is youngest YROT of args if not AI, or else AI addr.
Leakage contract: implicit transmitters handled by aforementioned prediction and resolution taint blocks as in STT, explicit transmitters refactored such that µpaths don’t vary based on data
Execution contract: Architect-defined visibility point (at head of ROB, or oldest unresolved branch)
SDO
Notes: Implementation detail – test via variability

## Slide 19: Speculative Privacy Tracking — MICRO ’21
STT modified with declassification pass back based on implicit instruction functions for leakage propagation
SNI – does not protect against things that haven’t already leaked
DOES NOT discriminate between partial vs full leakage of an instruction
Delayed execution protection policy
SPT

## Slide 20: SimSpect specification
Protection set: all memory.
Propagation: Untainting when an operand is transmitted by a non-speculative transmit or branch, followed by propagation:
    Forward output untainting: if all operands untainted, output untainted
    Backward input untainting: if mov or invertible arith, a singular tainted input is untainted if everything else is
    STL load address transmission untainting
Leakage contract: explicit transmitter set user-defined, implicit transmitters also handled by aforementioned prediction and resolution taint blocks
Execution contract: Visibility point
SPT
Notes: STT. strict dependency + YROT untaint calculus — a. Any speculative access instruction is tainted. b. Other output is tainted if input is tainted. Untainted once YROT nonspeculative. YROT is youngest YROT of args if not AI, or else AI addr.

## Slide 21: Mechanisms to exercise
If we don’t just want a conservative non-taint logic, need to differentiate between instructions at a finer granularity such that we can properly cover the untainting
SPT

## Slide 22: Known bugs
Subregister writing
    X86 artifact that you can write subregisters, unprotects half-written secrets but then the unaligned load can leak information
    Gem5 issues 2 separate calls and SPT unprotects both loads becase it has byte granularity protection but assumes the memory access hits the whole thing
Rename stage
    Default to mark registers as unprotected, then protect when renamed
SPT

## Slide 23: RevealConceal — Micro ’23
Tracking non-speculative leakage is a good security definition, but carries a lot of overhead in tracking complexity (SPT)
Insight: the majority of these non-speculative leakage events are pointer dereferences (load address transmissions)
STT has loss of MLP in prohibition of load-load dependencies
Only track pointer dereference s.t. we can limit overhead
ReCon

## Slide 24: ReCon-STT SimSpect specification
Protection set: all memory. Propagation: STT propagation – data leaked non-speculatively by a load-load pair address transmission
Leakage contract: explicit transmitter set user-defined, implicit transmitters also handled by aforementioned STT prediction and resolution taint blocks
Execution contract: Shadows, as in DoM
ReCon
Notes: STT. strict dependency + YROT untaint calculus — a. Any speculative access instruction is tainted. b. Other output is tainted if input is tainted. Untainted once YROT nonspeculative. YROT is youngest YROT of args if not AI, or else AI addr.

## Slide 25: ReCon-NDA SimSpect specification
Protection set: all memory. Propagation: STT propagation – data leaked non-speculatively by a load-load pair address transmission
Leakage contract: all transmitters
Execution contract: Shadows, as in DoM
ReCon
Notes: STT. strict dependency + YROT untaint calculus — a. Any speculative access instruction is tainted. b. Other output is tainted if input is tainted. Untainted once YROT nonspeculative. YROT is youngest YROT of args if not AI, or else AI addr.

## Slide 26: Known bugs
STT load order bug
    Stalls transmitters until oldest load that the sensitive op depends on has become nonspeculative (should be youngest)
Secondary STT bug
    Untaints register when the youngest load it depends on reads unprotected memory, but if there are multiple you must check all speculative loads it depends on
Memory unprotection protection set tracking bug
    Recon unprotects secret memory when an interleaved store makes the memory secret but its prior value leaks later
ReCon

## Slide 27: STT load order bug
ReCon
Recon stalls transmitters until oldest load that the sensitive operand depends on, should be the youngest.
Load sec -> a
Load mem[a] -> c
Load b -> a
s
Protection set
{sec}
{sec}
{sec, a}
{sec}
co
rf
Basic instructions
Edges
Transmit a
A protected item (a) leaks speculatively
po
po

## Slide 28: Known bug in memory unprotection
Hypothesis: Consider the equivalence classes of arch. state tracked by a defense. Poor protection set tracking occurs when non-rf edges are misinterpreted to collapse equivalence classes
Equivalence set to the output of instruction i at its execution time = what state could be unprotected by transmission at i = i.(^(~rf+rf) & ^(~po))
Recon unprotects memory when it is leaked nonspeculatively despite there being an interleaved secret store.
Load m[a] -> b
Load m1 -> c
Load m1 -> a
1
3
4
Execution
Store sec -> m1
2
Instruction
Recon thinks m1 leaked, unprotects m1 and a, splits protection sets
Load [c] -> d
5
Sec leaked
s
{sec, m1}
{sec, b}
Protection set
(erroneous protection set)
Transmit a
Transmit c
{sec, m1, a}
{sec, m1, a}
{sec, m1, b}
{sec, m1, b, c}
{sec, b}
{sec, m1, b, d}
{sec, b}
fr
rf
rf
rf
1
3
2
4
5
rf
rf
rf
fr
Equivalence class 1, leaked and unprotected
Equivalence
class 2, not
leaked and protected
Misinterpreted fr edge
po
po
po
po
ReCon

## Slide 29: Secondary STT bug
ReCon
IN PROGRESS
bad execution:
prot m1
spec (true)
load ra from m1
spec (false)
load ra from m2
load rb from m\[ra] *leak ra*

## Slide 30: Doppelganger Loads — ISCA ’23
SDO helps with the MLP problem but doesn’t neatly conceal load address, just load timing behavior
Insight: predict load addresses with doppelganger loads that predict load address and load information from memory without predicating on speculative data
Threat-model transparent!
Doppelganger Loads

## Slide 31: DL-NDA SimSpect specification
Protection set: all memory. Propagation: strict dependency — a. Any speculative access instruction is protected. b. Other output is protected if input is protected
Leakage contract: Transmitter type irrelevant, should protect for all
Execution contract: Instructions are non-speculative at head of ROB, but also before head of ROB if ∄ older branches with unresolved target or address, and ∄ stores with unresolved address
Doppelganger Loads
Notes: STT. strict dependency + YROT untaint calculus — a. Any speculative access instruction is tainted. b. Other output is tainted if input is tainted. Untainted once YROT nonspeculative. YROT is youngest YROT of args if not AI, or else AI addr.

## Slide 32: DL-STT SimSpect specification
Protection set: all memory. Propagation: strict dependency + YROT untaint calculus — a. Any speculative access instruction is tainted. b. Other output is tainted if input is tainted. Untainted once YROT nonspeculative. YROT is youngest YROT of args if not AI, or else AI addr. (like DIFT)
Leakage contract: explicit transmitter set user-defined, implicit transmitters also handled by aforementioned prediction and resolution taint blocks
Execution contract: Architect-defined visibility point (at head of ROB, or oldest unresolved branch)
Doppelganger Loads

## Slide 33: DL-DoM SimSpect specification
Protection set: All registers and memory
Leakage contract: Protects against load-address transmission only
Execution contract: Protects instructions that fall under shadows:
    E-Shadows – instructions that can generate exceptions
    C-Shadows – control instructions with an unknown address or condition
    D-Shadows – load dependencies due to stores with unknown addresses because of STL forwarding
    M-Shadows – under strict memory models, load reordering could lead to squashes
Doppelganger Loads
Notes: STT. strict dependency + YROT untaint calculus — a. Any speculative access instruction is tainted. b. Other output is tainted if input is tainted. Untainted once YROT nonspeculative. YROT is youngest YROT of args if not AI, or else AI addr.

## Slide 34: Mechanisms to exercise
Under construction
Protean

## Slide 35: Non-applicable defenses
Todo