## Slide 1: SimSpect 1/23/2026

## Slide 2: SimSpect final pipeline design
Defense implementation
Defense specification
Implementation ISA
Tuning parameters
n abstract litmus tests
m concrete litmus tests (m>>n)
m speculation annotations
Translation to modeling syntax (manual)
- Leakage contract
- Exec. contract
- Prot. set
- Prot. mechanism
Initial execution model
- Defense is minimally leaky
- Defense is unique along certain axes
Defense-specific allowed leakage
Litmus test filters
Sort into modeling syntax-specific buckets (decide granularity)
Defense-specific choices for expansion priorities
Stage 1: Alloy Analyzer
Stage 2: Python and Java
Stage 3: C++, a bit of python
Pass 1: Specify instructions
- Start with speculation primitives, add them to annotation
- Then flesh out other ISA instructions from respective buckets, including xmits, add them to annotation
Consolidate and repeat tests into one large testing program
Instrument simulator with annotation- and testing program-derived prediction values
Run test program and inspect instruction order and predictions
Pass 2: Add interleave
- Add both on- (ALU) and off-path (any) interleaved instructions, priming downstream state to demonstrate change
Pass 3: Specify state
- Allocate reg and mem state from allowed list
- Note priming for interleaves
- Floating reg and mem should be unique or shared
Pass 4: Filtration
- Assign some method of prioritization based on including all test cases at a bare minimum, then which ISA instructions to expand upon, then can cut off testing at any point

## Slide 3: Updates overview
Apple
  Bit of a time sink last week, but glad to have the interviews over, they were technical, and also straddled DV and RTL (Sendil, Hangkyu, Johns)
  I accepted offer, note to discuss more with you and John Pape or anyone else about the content that does/does not belong to Apple post internship
  Mostly not code but the framework of categorizing leakage — I know nothing about IP but since you and Nick came up with that
Coding
  Two fronts right now, LLVM register chaos and Gem5 confusion
  Even simplest (-o0) LLVM->X86 degrades information I want to fix
Deliverables

## Slide 4: Writing deliverables
By Monday 1/26 I will send you the intro, background + related work
By Friday 1/30 I will send you the technical sections
  Formal model
    Four operative definitions
    A chart of how they apply to all our studied defenses
    Description of how they work to define violating traces as seen in our execution model
  Test generation
    Description of Alloy structure
    Description of relaxations, framed similarly to Lustig paper

## Slide 5: LLVM progress
Different optimization passes:
  https://iitd-plos.github.io/col729/labs/lab1/lab1.html
-O0 – no optimization (still does dead code elim, x86 instruction selection, spilling (BAD), stack layout, nops
-O1 – more scheduling
-O2 – for production builds, vectorization and gets rid of variables and code blocks
-O3, -Oz, -Os aggressive, size aggressive, size

## Slide 6: LLVM progress
I want to control register allocation so I have to do it manually??
I was reading about forcing certain inline x86 in the LLVM but it still optimizes, I would have to fence
Issue is the spilling and dead code elim
So I have new register algorithm

## Slide 7: LLVM progress
Mapping from alloy reg  loc where loc is physical reg like %r12 or else a stack slot [rbp-0x20]
Walk PO, for each instruction
  Make sure inputs are in temp phys reg, assign one if needed
  Compute result into a temp reg
  Wb to dest reg location, FLAG IF SPILL -> that test fails
Maintain freelist of registers (not sure if there’s a way to free them though, the ones that are just allocated for one use should be allowed)
Came to the conclusion that it doesn’t matter if we generate a second violating path so I’m no longer tracking that (chart of second path causing false positive vs adding important information)
  Case where both are true
Maintain determinism in ordering

## Slide 8: Enumeration questions
Sending complexity back to alloy??? If I constrain registers there and fill each register
I’m also doing a slow alloy debug via manual inspection of identical x86 programs (figuring out how to tell Alloy to ignore certain sigs)

## Slide 9: Gem5
Still trying to tinker with the store address predictor
Store_set.cc and store_set.h
It isn’t affecting anything so I’m trying to debug that right now

## Slide 10: Example
STT (upon commit)
Execution contract:
Speculation = uncommitted
Protection set:
All memory
Leakage function: all load’s addresses
+ branch and other xmit’s inregisters
Protection mechanism (propagation): static

## Slide 11: Example
Known bug:
mov a [b]
mov c [a] // committed, unprot [b]
mov a [d] // uncommitted, load a secret
mov e [a] // leak
committed
uncommitted
load r1 [r0]
Uncommitted, unresolved
load r2 [r1]
Uncommitted, unresolved
operands
inaddr
inmem
outreg
inaddr
inmem
outreg
spo
r0
[r0]
r1
[r1]
r2
instructions
state
Orange is transmitter
Purple protected state
ddi
rf

## Slide 12: Example
Known bug:
mov a [b]
mov c [a] // committed, unprot [b]
mov a [d] // uncommitted, load a secret
mov e [a] // leak
committed
uncommitted
load r1 [r0] // uncommitted, unresolved
load r2 [r1] // uncommitted, unresolved

## Slide 13: Example
Known bug:
mov a [b]
mov c [a] // committed, unprot [b]
mov a [d] // uncommitted, load a secret
mov e [a] // leak
committed
uncommitted
mov r1 [r0] // uncommitted, unresolved
mov r2 [r1] // uncommitted, unresolved

## Slide 14: Example
Known bug:
mov a [b]
mov c [a] // committed, unprot [b]
mov a [d] // uncommitted, load a secret
mov e [a] // leak
committed
uncommitted
mov r1 [r4] // committed, resolved
mov r3 [r1] // committed, resolved
mov r1 [r0] // uncommitted, unresolved
mov r2 [r1] // uncommitted, unresolved

## Slide 15: Example
Known bug:
mov a [b]
mov c [a] // committed, unprot [b]
mov a [d] // uncommitted, load a secret
mov e [a] // leak
committed
uncommitted
mov r1 [r4] // committed, resolved
mov r3 [r1] // committed, resolved
mov r1 [r0] // uncommitted, unresolved
mov r2 [r1] // uncommitted, unresolved

## Slide 16: Example
Known bug:
mov a [b]
mov c [a] // committed, unprot [b]
mov a [d] // uncommitted, load a secret
mov e [a] // leak
committed
uncommitted
mov r1 [r4] // committed, resolved
mov r3 [r1] // committed, resolved
mov r1 [r0] // uncommitted, unresolved
mov r2 [r1] // uncommitted, unresolved

## Slide 17: Example

## Slide 18: SimSpect 1/9/2026
Where are we?

## Slide 19: SimSpect final pipeline design
Defense implementation
Defense specification
Implementation ISA
Tuning parameters
n abstract litmus tests
m concrete litmus tests (m>>n)
m speculation annotations
Translation to modeling syntax (manual)
- Leakage contract
- Exec. contract
- Prot. set
- Prot. mechanism
Initial execution model
- Defense is minimally leaky
- Defense is unique along certain axes
Defense-specific allowed leakage
Litmus test filters
Sort into modeling syntax-specific buckets (decide granularity)
Defense-specific choices for expansion priorities
Stage 1: Alloy Analyzer
Stage 2: Python and Java
Stage 3: C++, a bit of python
Pass 1: Specify instructions
- Start with speculation primitives, add them to annotation
- Then flesh out other ISA instructions from respective buckets, including xmits, add them to annotation
Consolidate and repeat tests into one large testing program
Instrument simulator with annotation- and testing program-derived prediction values
Run test program and inspect instruction order and predictions
Pass 2: Add interleave
- Add both on- (ALU) and off-path (any) interleaved instructions, priming downstream state to demonstrate change
Pass 3: Specify state
- Allocate reg and mem state from allowed list
- Note priming for interleaves
- Floating reg and mem should be unique or shared
Pass 4: Filtration
- Assign some method of prioritization based on including all test cases at a bare minimum, then which ISA instructions to expand upon, then can cut off testing at any point

## Slide 20: Rough progress
Defense implementation
Defense specification
Implementation ISA
Tuning parameters
n abstract litmus tests
m concrete litmus tests (m>>n)
m speculation annotations
Translation to modeling syntax (manual)
- Leakage contract
- Exec. contract
- Prot. set
- Prot. mechanism
Initial execution model
- Defense is minimally leaky
- Defense is unique along certain axes
Defense-specific allowed leakage
Litmus test filters
Sort into modeling syntax-specific buckets (decide granularity)
Defense-specific choices for expansion priorities
Stage 1: Alloy Analyzer
Stage 2: Python and Java
Stage 3: C++, a bit of python
Pass 1: Add interleave
- Add both on- (ALU) and off-path (any) interleaved instructions, priming downstream state to demonstrate change
Consolidate and repeat tests into one large testing program
Instrument simulator with annotation- and testing program-derived prediction values
Run test program and inspect instruction order and predictions
Pass 2: Specify instructions
- Start with speculation primitives, add them to annotation
- Then flesh out other ISA instructions from respective buckets, including xmits, add them to annotation
Pass 3: Specify state
- Allocate reg and mem state from allowed list
- Note priming for interleaves
- Floating reg and mem should be unique (size issues)
Pass 4: Filtration
- Assign some method of prioritization based on including all test cases at a bare minimum, then which ISA instructions to expand upon, then can cut off testing at any point

## Slide 21: Design questions
What is model syntax?
Which dimensions to relax along, because not everything must be minimal, interesting compound cases?
Model-domain symmetry breaking – which axes do we care about
Enumeration-domain symmetry breaking – which axes do we care about
Prioritization ranking? Iterate through abstract tests starting with a few of each, then prioritize other copies lower?
Register list reaching capacity (eg instr execution of len 5, + 2 interleave can deal with 21 registers)
Which ISAs
How to categorize, do we use all instructions
Annotation format – to check the correct xmit state later
Which knobs to give to user
Size of interleaves
Limit to transmitters we can track? No because not like AMuLeT
Register and memory domains
Cache initial state
Order of enumeration passes?
Number of times to run things
Detail handled by protection mechanism
Which defenses to test
How to add relevant state without messing up leakage flow?

## Slide 22: Design questions
Stage 1:
  Model syntax
  Which defenses to test
  Detail of protection mechanism
  Relaxation dimensions, compound minimal cases?
  Model-domain symmetry breaking
Stage 2:
  Which ISAs to support
  How to categorize instructions, leave any out?
  Which knobs to give a user
  Order of the enumeration passes
  Size of interleaves
  How to add relevant state without messing up leakage flow
  Annotation format compatible with later probing
  Register list capacity if everything is unconstrained (don’t want extra dependencies)
  Test prioritization after the fact
  Repetitive tests (through multiple forms of modification converging)
Stage 3:
  Register and memory domains
  Cache initial state
  Number of times to run things
Notes: These are all design decisions we are making
Most of them figured out, but I want to be able to defend why we did each thing in the paper or if someone asks

## Slide 23: Design questions
Stage 1:
  Model syntax
  Which defenses to test
  Detail of protection mechanism (incl committed) (Protean complication)
  Relaxation dimensions, compound minimal cases? ???
  Model-domain symmetry breaking
Stage 2:
  Which ISAs to support - x86
  How to categorize instructions, leave any out?
  Which knobs to give a user
  Order of the enumeration passes – I think this is fixed
  Size of interleaves
  How to add relevant state without messing up leakage flow (recalculating flow)
  Annotation format compatible with later probing – I think done
  Register list capacity if everything is unconstrained (don’t want extra dependencies)
  Test prioritization after the fact
  Repetitive tests (through multiple forms of modification converging) I think I designed so this won’t happen
Stage 3:
  Register and memory domains
  Cache initial state
  Number of times to run things
Notes: These are all design decisions we are making
Most of them figured out, but I want to be able to defend why we did each thing in the paper or if someone asks

## Slide 24: Model
Nodes:
Instructions:
    Xmit
      Ld
      Str
      Br
      other
    Non-xmit
      Br
      other
State: reg, mem
Booleans:
Committed (out of ROB, non-spec)
    Contiguous at end of SPO
Resolved
    Br knows target and condition
    Ld str know addr
Edges:
Ordering
    Po: i->i
    Spo: i->i
    Rf, ddi: i->i
Labeling
    In_addr, in_reg, in_mem, out_reg, out_mem: i->state
    Bool: i->bool
Relaxations
Remove instruction
Remove operand
Remove committed
Remove resolved

## Slide 25: Defenses
STT [Yu+, MICRO ’19]
SpecShield [Barber+, PACT ’19]
NDA [Weisse+, MICRO ’19]
Delay-on-Miss [Sakalis+, ISCA ’19]
SDO [Yu+, ISCA ’20]
SPT [Choudhary+, MICRO ’21]
Recon [Aimoniotus+, MICRO ’23]
Doppelgänger loads [Kvalsvik+, ISCA ’23]
Protean
All implemented stage 1 except Protean, how to represent forced protsets from compiler with only an update rule?
Mostly just using STT and NDA for stage 2 initial testing, but should be generally applicable, except need to specify tuning parameters
Amulet tests:
InvisiSpec, CleanupSpec, STT, and SpecLFB
STT prog size | Tests
2 | None
3 | 72
4 | 132
5 | 210

## Slide 26: Other things
  Updates:
  Got rid of json factoring, I just have a model for each thing, could allow me to add more custom relaxations down the line if necessary
  Had to go back to the hacky propagation again
  secret set in the presentation
  Have some good figures coming up
  Writing, made progress on intro and started some of the technical sections. Can I send you an intro draft soon
Apple final round Monday
  Good talk with Jon Tyler about test design for HSCs
Notes: In order commits changing prot set in different order

## Slide 27: Example
STT (upon commit)
Execution contract:
Speculation = uncommitted
Protection set:
All memory
Leakage function: all load’s addresses
+ branch and other xmit’s inregisters
Protection mechanism (propagation): static except committed loads unprotect their address in

## Slide 28: Example
Known bug:
mov a [b]
mov c [a] // committed, unprot [b]
mov a [d] // uncommitted, load a secret
mov e [a] // leak
committed
uncommitted
load r1 [r0]
Uncommitted, unresolved
load r2 [r1]
Uncommitted, unresolved
operands
inaddr
inmem
outreg
inaddr
inmem
outreg
spo
r0
[r0]
r1
[r1]
r2
instructions
state
Orange is transmitter
Purple protected state
ddi
rf

## Slide 29: Example
Known bug:
mov a [b]
mov c [a] // committed, unprot [b]
mov a [d] // uncommitted, load a secret
mov e [a] // leak
committed
uncommitted
load r1 [r0] // uncommitted, unresolved
load r2 [r1] // uncommitted, unresolved

## Slide 30: Example
Known bug:
mov a [b]
mov c [a] // committed, unprot [b]
mov a [d] // uncommitted, load a secret
mov e [a] // leak
committed
uncommitted
mov r1 [r0] // uncommitted, unresolved
mov r2 [r1] // uncommitted, unresolved

## Slide 31: Example
Known bug:
mov a [b]
mov c [a] // committed, unprot [b]
mov a [d] // uncommitted, load a secret
mov e [a] // leak
committed
uncommitted
mov r1 [r4] // committed, resolved
mov r3 [r1] // committed, resolved
mov r1 [r0] // uncommitted, unresolved
mov r2 [r1] // uncommitted, unresolved

## Slide 32: Example
Known bug:
mov a [b]
mov c [a] // committed, unprot [b]
mov a [d] // uncommitted, load a secret
mov e [a] // leak
committed
uncommitted
mov r1 [r4] // committed, resolved
mov r3 [r1] // committed, resolved
mov r1 [r0] // uncommitted, unresolved
mov r2 [r1] // uncommitted, unresolved

## Slide 33: Example
Known bug:
mov a [b]
mov c [a] // committed, unprot [b]
mov a [d] // uncommitted, load a secret
mov e [a] // leak
committed
uncommitted
mov r1 [r4] // committed, resolved
mov r3 [r1] // committed, resolved
mov r1 [r0] // uncommitted, unresolved
mov r2 [r1] // uncommitted, unresolved

## Slide 34: SimSpect final pipeline design
Defense implementation
Defense specification
Implementation ISA
Tuning parameters
n abstract litmus tests
m concrete litmus tests (m>>n)
m speculation annotations
Translation to modeling syntax (manual)
- Leakage contract
- Exec. contract
- Prot. set
- Prot. mechanism
Initial execution model
- Defense is minimally leaky
- Defense is unique along certain axes
Defense-specific allowed leakage
Litmus test filters
Sort into modeling syntax-specific buckets (decide granularity)
Defense-specific choices for expansion priorities
Stage 1: Alloy Analyzer
Stage 2: Python and Java
Stage 3: C++, a bit of python
Pass 1: Add interleave
- Add both on- (ALU) and off-path (any) interleaved instructions, priming downstream state to demonstrate change
Consolidate and repeat tests into one large testing program
Instrument simulator with annotation- and testing program-derived prediction values
Run test program and inspect instruction order and predictions
Pass 2: Specify instructions
- Start with speculation primitives, add them to annotation
- Then flesh out other ISA instructions from respective buckets, including xmits, add them to annotation
Pass 3: Specify state
- Allocate reg and mem state from allowed list
- Note priming for interleaves
- Floating reg and mem should be unique (size issues)
Pass 4: Filtration
- Assign some method of prioritization based on including all test cases at a bare minimum, then which ISA instructions to expand upon, then can cut off testing at any point

## Slide 35: SimSpect final pipeline design
Defense implementation
Defense specification
Implementation ISA
Tuning parameters
n abstract litmus tests
m concrete litmus tests (m>>n)
m speculation annotations
Translation to modeling syntax (manual)
- Leakage contract
- Exec. contract
- Prot. set
- Prot. mechanism
Initial execution model
- Defense is minimally leaky
- Defense is unique along certain axes
Defense-specific allowed leakage
Litmus test filters
Sort into modeling syntax-specific buckets (decide granularity)
Defense-specific choices for expansion priorities
Stage 1: Alloy Analyzer
Stage 2: Python and Java
Stage 3: C++, a bit of python
Pass 1: Specify instructions
- Start with speculation primitives, add them to annotation
- Then flesh out other ISA instructions from respective buckets, including xmits, add them to annotation
Consolidate and repeat tests into one large testing program
Instrument simulator with annotation- and testing program-derived prediction values
Run test program and inspect instruction order and predictions
Pass 2: Add interleave
- Add both on- (ALU) and off-path (any) interleaved instructions, priming downstream state to demonstrate change
Pass 3: Specify state
- Allocate reg and mem state from allowed list
- Note priming for interleaves
- Floating reg and mem should be unique or shared
Pass 4: Filtration
- Assign some method of prioritization based on including all test cases at a bare minimum, then which ISA instructions to expand upon, then can cut off testing at any point